## Slide 1
BMIT2123 INTERNET OF THINGS | PART I SYSTEM PROTOTYPE PROPOSAL
AgriSense
A Precision Farming System for Outdoor Canopy Plantations
Group Members: Foo Tun Wei(Leader) · Kueh Jian Wei · Heng Jing Le · Tey Ying Heng
Programme & Group: RSD2S3 G3
1

## Slide 2
OVERVIEW
Agenda
01
Background & Problem Statement
02
System Overview & Objectives
03
Targeted Users
04
System Architecture
05
Functional Modules 1–4
06
Cross-Module Design Standards
07
Data Contract, Plant Profile & Override
08
Task Allocation, Priorities & Timeline
2

## Slide 3
BACKGROUND
The Problem with Manual Outdoor Plantation Care
Blind Watering
Fixed-schedule irrigation ignores rain and humidity, wasting water or under-feeding crops.
Weather Blind Spots
Sudden rain can still trigger unnecessary irrigation if the system only reads soil moisture.
Late Health Detection
Leaf stress or disease is usually noticed only during physical rounds, often after visible damage.
No Historical Insight
Without logged data, managers cannot analyse trends or plan resource use ahead of time.
3

## Slide 4
(A) SYSTEM TITLE
AgriSense: Precision Farming System
AgriSense connects ESP32 sensors and actuators with a laptop, HiveMQ, Node-RED and Supabase — combining weather-aware irrigation, climate control, low-water protection and crop-health warnings.
Rain-Aware Irrigation
Use soil moisture, humidity and a weather forecast — not a hardware rain sensor.
Low-Water Safety
Force the pump OFF whenever the calibrated tank level reaches the safety threshold.
Historical Monitoring
Log sensor history, pump runtime estimates and crop-health images for review.
Crop-Flexible Design
Switchable Plant Profiles let the same system adapt to different crops.
4

## Slide 5
(B) DESCRIPTION & TARGETED USERS
Who Is AgriSense For?
AgriSense is deployed on the plantation's existing canopy-sheltered outdoor plot. It targets everyone involved in day-to-day operations and planning:
Farm Owners / Managers
Get a live overview of plot conditions and resource usage to make faster decisions.
Field Workers / Technicians
Receive actionable alerts (e.g. "Tank low", "Crop stress detected") instead of walking the whole site.
Agronomists / Analysts
Use logged trends (moisture, climate, growth photos, resource usage) to study crop health and plan ahead.
Deployment setting: Outdoor plot under a fixed protective canopy — sheltering electronics and the webcam from direct rain/sun while still allowing natural light and airflow.
5

## Slide 6
(B) SYSTEM OVERVIEW DIAGRAM
Overall System Architecture
One ESP32 runs Modules 1–3; the Laptop runs Node-RED and Module 4, linked through MQTT and Supabase
EXTERNAL DATA · Open-Meteo forecast → Node-RED weather decision
EDGE LAYER · ESP32 + LAPTOP
1 — Smart Irrigation
Soil + humidity + forecast → pump; AUTO/MANUAL + safety lock
2 — Climate Control
DHT11 + LDR → fan + prototype grow-light LED
3 — Water Tank & Resource Mgmt
Water-level brick → calibrated % + pump lock + runtime estimate
4 — Farm Safety & Crop Health
USB webcam (Laptop) + MQTT climate → warning + growth diary
MQTT + CLOUD
HiveMQ + Supabase
HiveMQ carries live telemetry and control; Supabase stores readings, alerts and growth-diary images.
DASHBOARD + NODE-RED
GitHub dashboard for live control · Node-RED weather logic on Laptop
Live status, trend charts & growth photo timeline
Rule-triggered log + module Health Status
Dashboard and MQTT alerts with module health
Manual control for pump, fan and prototype light
Priority: LOW-WATER LOCK > MANUAL > AUTO. Module 4 warns only; no automatic treatment.
6

## Slide 7
(C) FUNCTIONAL MODULE — MEMBER 1
Smart Irrigation Management
Weather-aware watering with AUTO/MANUAL control and a hard low-water lock
Module 1
Kueh Jian Wei
ESP32
Owns full Input → Process → Output loop
Input
Soil moisture · humidity from Module 2 · Weather API forecast through Node-RED · low-water lock from Module 3.
Process — Rule-01 (Irrigation)
Dry soil + no rain expected → Pump ON. Rain expected soon → delay. Moist soil → Pump OFF.
Process — Control Priority
LOW-WATER LOCK > MANUAL > AUTO. Automatic rules never overwrite MANUAL; the safety lock can still force Pump OFF.
Output & Design Note
Water pump + 16×2 LCD + dashboard alert + irrigation history. Safety feedback confirms the actual pump state.
7

## Slide 8
(C) FUNCTIONAL MODULE — MEMBER 2
Climate Control
Monitor temperature, humidity and light with confirmed prototype hardware
Module 2
Tey Ying Heng
ESP32
Owns full Input → Process → Output loop
Input
DHT11 (temperature/humidity) · LDR (raw light level).
Process — Rule-03
LDR below its calibrated raw threshold → ordinary yellow LED ON as a prototype grow-light indicator.
Process — Rule-04 / 04b
Temperature ≥ 30°C → fan ON; temperature ≤ 28°C → fan OFF, using hysteresis to avoid rapid switching.
Output
Fan + ordinary yellow LED (prototype indicator, not a real agricultural grow light); LCD and dashboard status.
8

## Slide 9
(C) FUNCTIONAL MODULE — MEMBER 3
Water Tank & Resource Management
One analog level sensor supports calibration, safety locking and honest usage estimates
Module 3
Heng Jing Le
ESP32
Owns full Input → Process → Output loop
Input
Analog High-Sensitivity Water Level Brick Sensor connected to ESP32 ADC1.
Process — Calibration & Safety
Map raw readings between measured empty/full points. At ≤15%, force Pump OFF and publish a non-bypassable lock.
Process — Runtime Estimate
Estimate water use from pump ON time only; label it as an estimate until a calibrated flow sensor is installed.
Output
Buzzer, LCD and dashboard warning; MQTT pump-lock state; water-level history and estimated usage.
9

## Slide 10
(C) FUNCTIONAL MODULE — MEMBER 4
Farm Safety & Crop Health Monitoring
One USB webcam, two uses: growth diary and early health warning — warns, doesn't act automatically
Module 4
Foo Tun Wei
Laptop + USB Webcam
Owns full Input → Process → Output loop
Input
USB webcam connected directly to Laptop · temperature/humidity subscribed through MQTT.
Process — Dual Use
Validate each image, archive it in the growth diary, then use HSV segmentation for green/yellow area percentages.
Process — Rule-06
Rising yellowing trend plus high humidity → higher prototype risk score and GREEN/AMBER/RED warning.
Output — Indicator + UI (by design)
ESP32 RGB light + buzzer receive MQTT status; dashboard and Supabase store warnings. Colour stress is a proxy — no diagnosis or automatic treatment.
10

## Slide 11
CROSS-MODULE DESIGN STANDARDS
Shared Standards Across All 4 Modules
Rule Table, not if-else
Keep each decision as Condition → Action with a rule ID, so the dashboard explains why an actuator changed.
Per-Module Health Status
Each module reports Healthy / Warning / Fault for its own hardware (e.g. "Pump: Healthy"), giving an at-a-glance system health view.
Trend, not just a Point Value
Dashboards show change over time (e.g. "Humidity 90% ↑ +10% past 3h") — because in real farming, the trend matters more than one reading.
Rule ID | Condition | Action
Rule-01 | Soil dry, no rain expected | Pump ON
Rule-02 | Soil dry, rain expected soon | Delay irrigation
Rule-05 | Water level ≤ 15% | Pump OFF + Lock
Example rules reflect weather-aware irrigation and the non-bypassable low-water lock:
11

## Slide 12
DATA CONTRACT & FLEXIBILITY
Data Contract · Plant Profile · Manual Override
Shared Data Contract
MQTT topics carry live values; Supabase stores a consistent history for the dashboard.
{
"module": "irrigation",
"value": 28,
"trend": "+5% (3h)",
"health_status": "Healthy",
"rule_triggered": "Rule-01",
"timestamp": "..."
}
Plant Profile
Business rules read their thresholds from the active profile — switch crops without touching code.
Parameter | Tomato | Chili
Soil Moisture | 40% | 35%
Temp Range | 24–30°C | 22–28°C
Humidity Max | 80% | 80%
Manual Override
Manual commands help testing, but never bypass the low-water safety lock.
AUTO Mode
(default)
User switches
to MANUAL
Direct actuator
control (e.g. Pump
ON 10s)
Returns to
AUTO Mode
Available for water pump, fan and the prototype grow-light indicator.
12

## Slide 13
(D) TASK ALLOCATIONS
Task Allocation
Member | Module | Key Responsibilities
Kueh Jian Wei Module 1 | Smart Irrigation | Soil moisture; humidity + forecast rules; AUTO/MANUAL pump control and low-water lock.
Tey Ying Heng Module 2 | Climate Control | DHT11 temperature/humidity + LDR; fan and yellow LED prototype grow-light indicator.
Heng Jing Le Module 3 | Water Tank & Resource Mgmt | Water-level calibration and percentage; pump lock; runtime usage estimate and history.
Foo Tun Wei Module 4 | Farm Safety & Crop Health Monitoring | Laptop + webcam; validation, HSV trends/risk, MQTT alerts and Supabase growth diary.
13

## Slide 14
RISK MANAGEMENT
Development Priority: MVP First, Stretch Later
Ensures a stable, complete demo even if advanced features run out of time
MUST-HAVE (MVP)
ESP32 Modules 1–3: sensor → rule → output loops
Laptop OS platform: Node-RED + Python/OpenCV
AUTO/MANUAL control with low-water priority
Weather API decision through Node-RED
Module 4 warnings + Supabase growth diary
2 Plant Profiles (Tomato, Chili) — fixed presets
STRETCH (If Time Allows)
More growth images + adjustable capture interval
Trend arrows across all dashboard widgets
Editable Plant Profiles from the dashboard
Optional notification integration
Optional calibrated flow sensor for precise volume
Additional calibrated cameras and lighting checks
14

## Slide 15
CONCLUSION
Expected Outcomes
Water Savings
Rain-aware irrigation avoids blind over-watering compared to fixed-schedule systems.
Traceable Monitoring
Supabase logs sensor history, pump-runtime estimates and growth images without claiming precise flow.
Faster, Safer Response
Low-water lock and crop-health warnings guide inspection; Manual control remains subordinate to safety.
Scope refined · implementation aligned
15